## Slide 1: CLASS WEB SITE: http://upmcsms.weebly.com/
Updated with Lecture Notes

## Slide 2: Named Data Networking (NDN)
Introduction to NDN

## Slide 3: Named Data Networking (NDN)
http://named-data.net  http://github.com/named-data

## Slide 4
IP
Host-centric
addressing
NDN
Data-centric
addressing

## Slide 5: Is It Deployed?
Deployable now as an overlay (TCP, UDP) or on Layer 2 transport
C, Java, Python, Javascript libraries
http://github.com/named-data
Testbed of 15 routers, including 5 on Internet2 / GENI
http://ndnmap.arl.wustl.edu/

## Slide 6: Run a Bit of NDN in your Browser Now
tinyurl.com/ndnrouting
tinyurl.com/ndnsensor
* - Requires working connection to current Internet.

## Slide 7: Telephone Network was the 1st Communication System
Focus on building and connecting the wires

## Slide 8: IP Revolutionized the Communication System
Internet Protocol (RFC791): Focused on delivering packets to destination host

## Slide 9: NDN: Focus on Data
Abstracting away the notion of “host”
Superset of host-to-host communication model

## Slide 10: Two Problems with Current Internet
Focus is on end-point communication
  Artifact of original thinking: share resources, not content
  Login to fast machine, access to the tape drive, the printer, etc.
Security
  To get data, you build a secure path
  Once you authenticated with the server, you trust the content

## Slide 11: New Communication Paradigm
Users today care about content, not the servers
Accessing the server is a by-product of the need to retrieve the desired content
  If the server is down, no access to the content
But what if the content was available from other places (e.g., my neighbor)?
We do a lot of this already with HTTP
  URLs, CDNs, caches, etc.

## Slide 12: Two Focal Points in NDN
Focus on the what not the where
Secure the data not the container

## Slide 13: NDN Operation
Interest packets
Data packets
Enhanced Forwarding
  Pending Interest Table (PIT)- new!
  Content Store (CS) – new!
  Forwarding Information Base (FIB) – similar to IP

## Slide 14: The IPv4 Datagram Format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.

## Slide 15: Two Simple Changes
ver
length
32 bits
data
(variable length)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
Delete the Source. Named Data Networking does not have sources
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
Delete the Destination. Named Data Networking does not have destinations
IPv6 killed these already

## Slide 16: NDN Packets
Content Name: Identifies the data I want to receive
Selector: identifier publisher, etc
Nonce
Content Name: Identifies the data in this packet
Signature: Required for all packets
Nonce
Data
Interest Packet
Data Packet

## Slide 17: NDN Forwarding: Interests
Interest: Content Name (CN) = X
Forward interest towards Publisher (X)
Mark incoming faces as wanting X (lay down breadcrumbs)
Merge same interests for X
Publisher
For X
Interest

## Slide 18: NDN Forwarding: Data
Data: Content Name (CN) = X Forward Data back to where interests came from
  Follow the breadcrumbs back to requestors
  Delete breadcrumbs
Duplicate at appropriate routers
Cache data at each router
Publisher
For X
Data

## Slide 19: Forwarding Process

## Slide 20: Comparison with IP Packet Forwarding

## Slide 21: NDN Interest Forwarding
get /parc.com/videos/WidgetA.mpg/v3/s2
/parc.com/videos/…../mpg/v3/s2 0
P
get /parc.com/videos/WidgetA.mpg/v3/s2
2

## Slide 22: NDN Data Forwarding
/parc.com/videos/…../mpg/v3/s2 0 2

## Slide 23: Summary
Route on content names
Content from anywhere: not just the producer
“Breadcrumbs” & de-duplication of requests
Cache retrieved data in Content Store (CS)
? /nytimes.com/today

## Slide 24: Hitting Cached Data
Interests only go so far until they find the data
Cached data can satisfy requests efficiently
Publisher
For X
X was cached here

## Slide 25: Multipath Interest Forwarding
Interests may be forwarded opportunistically to many destinations
  Strategy Layer
Data may be concurrently retrieved from multiple places
Publisher
For X
Interest
Repository
That may have X

## Slide 26: Example: Delivering Mail
Interest: I have mail for you
Interest: Give me your mail
Data: here’s my mail
Mail server
Mail client

## Slide 27: The Power of Naming
Naming can fetch the data transparently regardless of location
  Requests can go to appropriate place
Naming can result in generation of new data
  Can ask for data that does not yet exist!

## Slide 28
Experiment Topology

## Slide 29: NDN and Anonymity
NDN has no endpoint addresses – names in interests and data packets are ephemerally associated with incoming/outgoing faces
Info retrievable at a router:
  PIT – interest/data names and associated face information; in-memory, ephemeral (~RTT)
  Content Store – data names, no face information; in-memory, ephemeral (~nRTT)
  Attached storage (repo) – data names, no face information; on non-volatile memory, long-lived
Individual endpoints, however, engaged in a private conversation can still be identified by their names

## Slide 30: In NDN Vantage Point Matters
Regional ISP A
? /nytimes.com/today
AT&T
Regional ISP B
Vantage
Point A
Vantage
Point B
Vantage
Point C
Vantage
Point D
Information aggregation increases
and user targeting decreases going
from vantage points A – E
In IP it’s the opposite
Vantage
Point E
Notes: Consumer modems/routers may connect to neighborhood aggregator
Wiretap at ISP level has no info about where request came from
Problem made worse intermediate ISPs
Must drill down closer, into neighborhood and even home level to get info

## Slide 31: Recap
In NDN routers hold ephemeral name-to-interface associations – no e2e associations
Vantage point matters
Caching may satisfy interests before they reach your vantage point
Multipath may divert interests away from your vantage point
But private parties still visible on the wire

## Slide 32: DDoS Attacks
Classic DDoS is not possible
  Cannot send packets without interests
However, can still do Interest packet flooding
  Standard push-back defenses still possible
  Smart decisions based on parsing names
In general, NDN raises the bar

## Slide 33: Congestion Control
Use lessons learned from TCP – mechanisms carry over
  Define congestion window just like TCP
  Send interests that fall within the congestion window
  Use similar AIMD behavior
Note that receiver window is not needed – receiver pulls what it wants

## Slide 34: Key Distribution
No single way to distribute keys
  Key distribution outside the architecture
  Certificates, consensus, out-of-band, applications are free to implement anything that works
  Packets tell you how to get the key (or may even carry the key with them)
Key delegation
  Example: www.nytimes.com can delegate keys to editors for www.nytimes.com/sports, www.nytimes/com/business, etc.

## Slide 35: Conclusions
NDN preserves the hourglass shape of IP but with names at the narrow waist
Architecture focused on the what, not the where
New forwarding mechanisms enable multipath, multicast and other group operations
All content is signed
More at http://www.named-data.net/

## Slide 37: Backup slides

## Slide 38: Naming the Content
Client requests www.nytimes.com/today
Interests go out for each packet:
  www.nytimes.com/today/packet1
  www.nytimes.com/today/packet2
  …
Routers forward based on www.nytimes.com prefix (longest prefix match, just like IP)
Data is pulled and cached one packet at a time
Each packet contains information on how to retrieve the signing key

## Slide 39: Communication by Names
Producer announces data prefix
  e.g., www.nytimes.com/
Consumer sends interest
Producer replies with data
Applications using names
Delivering packet by IP addresses
Translation
Applications using names
Delivering packets by names
Notes: At 3000 feet view:

## Slide 40: Hitting Cached Data
Interests only go so far until they find the data
Cached data can satisfy requests efficiently
Publisher
For X
X was cached here

## Slide 41: Multipath Interest Forwarding
Interests may be forwarded opportunistically to many destinations
  Strategy Layer
Data may be concurrently retrieved from multiple places
Publisher
For X
Interest
Repository
That may have X

## Slide 42: Transparency in NDN
With a search warrant for a router, what can you discover about an ISP's users?
Assumption: warrant covers volatile and non-volatile memory

## Slide 43: Network Security in IP: why so Hard?
IP identifies interfaces/hosts
Current attempts aim at:
  Securing the box
  Securing the channel
  Securing an IP network by firewall
Securing the perimeter is hard
My net
Global Internet
Notes: How many papers published?
Are we better off today?

## Slide 44: 30 Years Down the Road
IP changed the world
A new world of applications & computing devices
Interconnections of computers
Moore’s Law & silicon revolution
Notes: All these were developed on top of point-to-point communication model
Twitter outages

## Slide 45: So Why a New Architecture?
What are the problems with the current Internet?
Are they worth re-designing the network?
With the current architecture being so entrenched, can we even deploy a new one?

## Slide 46: Evolution of Communication Abstraction
Telephone Network:
Focused on building the wires
Internet Protocol (RFC791): Focused on delivering packets to destination node
NDN: Focusing on retrieving data
Abstracting away the notion of “node”
Superset of node-to-node communication model
Notes: Evolution of the Web, REST on Internet

## Slide 47: A New Way to Think About Security
Secure the Content, Not the Channel!
  SSL, VPN, ssh tunnel, ToR, etc all focus on providing a secure channel
  Users don’t really care if the channel is secure, focus on the content
Require Authentication on All Content
  Security is not an option, its part of architecture
Encrypt the content if you don’t trust the channel
  Encryption is optional and applied where needed
Notes: How many papers published?
Are we better off today?